# Introduction
Decoder interface standards exist in order to aid in installation of decoders into vehicle system boards. Installation can performed by the vehicle manufacturer or separately by the individual modeler.
## Served Use Cases
The intent is that any decoder which conforms to the standard, from any manufacturer, will operate with any vehicle system board which conforms to the standard, from any manufacturer. Operate is further defined as not to cause any permanent damage of the decoder or vehicle system board.
## Unserved Use cases
It is not the purpose of the standard to ensure that every decoder and vehicle system board implements all of the possible features defined by the standard. Operation is limited to the features supported by the decoder and/or vehicle system board, as documented by the respective manufacturers.
# Annotations to the Standard
## General
### Introduction and Intended Use
#### References
Additional relevant references are found in S-9.1.1.5.
S-9.1.1.5 Next18 and Next18-S Decoder Interface
### Terms
### Requirements
It is important to note that a product is not required to implement all connections of the interface. A manufacturer may chose to omit certain features, for example the number of function outputs. It is incumbent on the manufacturer to document for users the supported features of their product(s).
## Mechanical Properties
The mechanical properties are provided in general terms so as not to codify into the standard any limit to alternative sources. Proper connector sources will result in a “click” of the two mating socket and plug components. TI-9.1.1 contains a list of manufacturer and part numbers for connector sources that have been tested for conformance to the standard.

### Plug Specification
### Socket Specifications
If a socket is provided that is terminated in wires, it is recommended that the wire colors follow the color codes defined in S-9.1.1.
## Electrical Properties
The Next18 defines pins 7 and 16 as logic-level outputs while the Next18-S defines pins 7 and 16 as speaker outputs. Because a sound variant decoder or vehicle system board can be physically connected to a non-sound variant vehicle system board or decoder, it is incumbent on the manufacturer to provide protection against damage should such a combination be used by a modeler. The vehicle system board manufacturer is only responsible for protecting the vehicle system board, while the decoder manufacturer is only responsible for protecting the decoder.
The standard does not prescribe how a manufacturer implements the protection. However, here are some suggestions that may offer adequate protection:
Next18 + Vehicle System Board With Sound
- On decoder, do not implement functions AUX5 and AUX6, leave unconnected.
- On decoder, add series resistor in-line to AUX5 and AUX6.
- On decoder, test in software for low impedance path (speaker) connected between AUX5 and AUX6. Disable outputs AUX5 and AUX6 if a low impedance path is discovered.
Next18-S + Vehicle System Board Without Sound
This use case is generally not a problem because the vehicle system board typically implements a high impedance transistor input to match AUX5 and AUX6 logic-level decoder outputs. Another options is for the system board to not implement AUX5 and AUX6 logic-level outputs.
### Next18 Pin Assignment
Note that AUX5 and AUX6 logic-level outputs (pins 7 and 16) are defined for Next18 only. Next18-S uses these same pins for Speaker A and Speaker B connections.
### Next18-S Pin Assignment
Note that Speaker A and Speaker B (pins 7 and 15) are defined for Next18-S only. Next18 uses these same pins for AUX5 and AUX6 logic-level outputs.
### Descriptions of Signals
V+ (pins 6 and 15 combined) is designed for a current rating of 1A. If a vehicle system board needs to consume more than 1A on V+, it may create its own version of V+ local to the vehicle system board. In the case that the vehicle system board does create its own version of V+, it is important that its local version not be connected to the interface V+ (pins 6 and 15). This could otherwise undermine the careful design of the decoder’s own internal power management.
### Use in Function Only Decoders
For the purpose of conformance, a function only decoder is a decoder which does not provide a motor control output on Motor + and Motor – (pins 2 and 11).
### Use of Interface with SUSI
This is the scenario where the Next18 or Next18-S interface is used for connection between a SUSI slave device and another host decoder acting in the role of SUSI master.
### Operation Without a Decoder